### SECTION 08710 Short Spec

GASKETING OF DOORS AND FRAMES (9-10-03)

1.04  	QUALITY ASSURANCE:

A.	Manufacturer’s Qualifications: To ensure and validate the proper closing, latching, sealing and securing of a door the manufacturer of gasketing shall provide a written program of Field Quality Assurance, acceptable to the architect that provides the site superintendent and installers with knowledge as to the industry acceptable standards for tolerances in manufacturing and field installation. The program shall create an audit trail of documentation for the inspection of pre-machined doors for machining and sizing, including hinge backset and depth of mortise, width and height. An “Installation Checklist” guideline shall also be furnished for verification of acceptability of related door, frame and hardware components prior to

installing gasketing.  These forms shall be part of the submittal process and shall be acknowledged by the site supervisor and returned to the manufacturer on a timely basis.

Evidence shall be provided that the STC specified and/or required by local code, as well as any requirements for smoke gasketing can be maintained under industry allowable tolerances for warp (AWI) and plumb (SDI). Evidence shall be provided that the gasketing system can meet this criteria and maintain this criteria under the Field Quality Assurance Standards.

If a substitute to the listed manufacturer for gasketing is desired , proof of compliance with the specification and with specific products shall be submitted prior to bid.

PART 2 - PRODUCTS:

2.01  	MANUFACTURERS:

A.	List of manufacturers represented in this section:

Door and Hardware Systems Inc. – www.dhsi-seal.com

13 Silver Street Rochester, New York  14611  TEL:585-235-8543

e-mail:	info@dhsi-seal.com       contact: Robert Rissone, President

1.	Door Bottoms:  Where door bottom seals are to be used, as listed in the hardware sets, provide DHSI #A-MDB3, #CS-36, #FS-M-36, #FS-MN-36 or “Secur-A-Seal” as selected and detailed. Where an undercut is desired at the guest entry between the bottom of the door and the flooring surface for HVAC design, provide the “AMU” option, “Allowance and Means for Undercut” and suffix the DHSI door bottom with “AMU”. If a “Solid Wood Lock Edge” is desired on a mortise door bottom, suffix part # with “SWE”.

2.	Meeting Stile Gasket:  When an astragal is not permitted due to the operation of hardware or by code restrictions, provide a self-adhesive seal at the meeting stiles.  Provide DHSI #SA surface astragal.   Where a mortise astragal is listed provide a DHSI #A-MA adjustable mortise astragal.

3.03  	FIELD QUALITY CONTROL

A.	Inspection:

1.	Any light passing the frame perimeter shall be cause for rejection (as per UL 1784 smoke test procedure).

2.	Door shall close from 70 degrees and latch freely without latch or hinge bind.

3.	The closing speed for ADA shall not exceed 3 seconds to within 3 inches of the latch position.  Lever torque shall not exceed ADA (taken from NFPA 101 Life Safety) of 15 inch pounds.

4.	Filing of strike plates to relieve lock bind is unacceptable (as per NFPA 80 = no field modifications of fire tested components is allowable).

5.	The "Industry Standards and Recommended Guidelines For Installation" shall govern field inspection.

6.	Field inspection and acceptance of product will be based upon the criteria of “Nationally Referenced Standards.”